## Slide 1
Midcontinent
Interactive
Digital
Carbon
Atlas and
Relational
DataBase
James A. Drahovzal, Lawrence H. Wickstrom, Timothy R.Carr, John A. Rupp, Beverly Seyler, and Scott W. White
Illinois State Geological Survey, Indiana Geological Survey, Kansas Geological Survey, Kentucky Geological Survey, Ohio Geological Survey

## Slide 2: Outline
Background
Goals of MIDCARB
MIDCARB State Differences
MIDCARB Database and Data Distribution
CO2 Sources
CO2 Sequestration Sinks
Benefits

## Slide 3: The Situation
Fossil fuels will remain the mainstay of energy production well into the 21st century
Without mitigation, antropogenic CO2 emissions to the atmosphere are predicted to more than double during the 21st century
Global environmental consequences
  Climate change
  Health issues

## Slide 4: Technical Approaches to and Factors in CO2 Management
Increase the efficiency of primary energy conversion systems
Use lower carbon or carbon-free fuels
Sequestration (Disposal)
  Geologic
  Critical Factors
    Cost
    Safety
Federal Rationale: Begin Research Now

## Slide 5
Midcontinent
Interactive
Digital
Carbon
Atlas and
Relational
DataBase

## Slide 6: MIDCARB Project Goals
Characterize
  Major Stationary Anthropogenic CO2 Sources
  Potential Geologic Sequestration Sites
  Costs and Benefits
Develop Relational/Spatial Databases
Serve the Results on the Internet
Why? A Planning Tool for Decisionmakers
Notes: The goals of the MIDCARB are to organize and enhance the critical information relative to CO2 sources and sequestration, and to develop the information technology tools needed to access, query, model, analyze, display and distribute natural resource data related to carbon management across five states, various organizations and numerous databases.

## Slide 7: State Perspective
Differences in
  Major Stationary CO2 Sources
  Geologic Sequestration Opportunities
  Relation of Sources to Sinks
  Economic Activity
  Fuel Sources and Mixes

## Slide 8: Illinois Electrical Energy Generation
30,367 Megawatts

## Slide 9: Kentucky Electrical Energy Generation
13,995 Megawatts

## Slide 10: CO2 Power Plant Emissions MIDCARB Consortium
US Census Bureau and DOE/EIA

## Slide 11: Kentucky Power Plants and Oil & Gas Fields
Coal
Oil
Natural gas
Hydroelectric
Proposed

## Slide 12: MIDCARB: Brings Together
Five Natural Resource Research Organizations
  Illinois, Indiana, Kansas, Kentucky, Ohio Geological Surveys
Large Natural Resources Databases
Relational Database Management Systems
Geographic Information Systems
Network (Web) Expertise
Notes: The five state Surveys each have extensive collections of data on prospective CO2 sinks. And, these organizations have all been working hard at providing this information via RDMS.

## Slide 13
Oil
Gas
Coal
Water
Rock
RDMS
Data

## Slide 14: MIDCARB: Brings Together
Five Natural Resource Research Organizations
  Illinois, Indiana, Kansas, Kentucky, Ohio
Large Natural Resources Databases
Relational Database Management Systems
Geographic Information Systems
Network (Web) Expertise
http://www.Midcarb.org
FOR MORE INFO...

## Slide 15: Kansas: CO2 Sources and Oil and Gas Resources

## Slide 16: MIDCARB: A Different Approach
Data is Distributed
  Differences in Table Structure
  Differences in Data Engines
User Access is Uniform
  Web
  Online Query
  Online Mapping

## Slide 17: MIDCARB Data Relationship Model
IL
IN
KY
KS
OH
Data
RDMS
Applications
Internet

## Slide 18
Midcontinent
Interactive
Digital
Carbon
Atlas and
Relational
DataBase
www.midcarb.org

## Slide 19: MIDCARB: Reservoir Characteristics
Ohio
Oil & Gas
Power Plants

## Slide 20: CO2 Source and Characterization
Anthropogenic Sources
  Power Plants
  Other Large Stationary Sources
Flue Gas
  Pressure, Temperature
  Concentrations, Output Patterns
Location in relation to:
  Sequestration Sites/Sinks
  Transportation Infrastructure

## Slide 21: MIDCARB CO2 Sequestration
Active and Depleted Oil and Gas Reservoirs
Unmineable Coal Beds
Deep Saline Aquifers
Unconventional Gas Reservoirs
  Deep, Poorly Known Reservoirs
  Devonian Black Shale

## Slide 22: CO2 Sequestration - Active Oil and Gas Reservoirs
CO2 Flooding (EOR Activities)
  Miscible and Immiscible in Oil Reservoirs
  Possible Pressure Maintenance in Gas Reservoirs
Benefits
  Increase Oil and Gas Production
  Sequester CO2: Lower Net Cost for Sequestration
Extensive Industry CO2 EOR Experience and Data
MIDCARB Data
  Reservoir Fluid and Rock Properties
  Geologic and Engineering Data

## Slide 23: CO2 Sequestration - Depleted Oil and Gas Reservoirs
Trapping
  Same Mechanisms that Trapped Original Oil and Gas
Benefits
  Proven Trap
  Existing Infrastructure
    Simpler
    Cheaper
  Storage over Geologic Time Periods
MIDCARB Data
  Reservoir Fluid and Rock Properties
  Geologic and Engineering Data

## Slide 24: CO2 Sequestration - Coalbed Methane
Trapping
  Adsorption of CO2 by Coal
  Displacement of CH4 by CO2 (2 CO2 : 1 CH4)
Double Benefit
  Sequestration of CO2
  Enhanced CBM Production
  Lowers Sequestration Net Costs
Growing Industry Experience and Data
  San Juan Basin
MIDCARB Data

## Slide 25: CO2 Sequestration - Deep Saline Aquifers
Trapping
  Immiscible Displacement of Brine Phase
  Dissolution (Minor) in the Brine
  Mineral Trapping
Benefits
  Includes Vast Areas of U.S.
  Large Reservoir Volumes
  Storage over Geologic Time Periods
Growing Industry Experience and Data
MIDCARB Data

## Slide 26: CO2 Geologic Sequestration Options
CO2 Improved Oil & Gas Recovery
CO2 Improved Coal Bed Methane Recovery
Deep Saline Aquifer
Underground Storage
Unmineable Coal
Modified from: http://www.spacedaily.com/news/greenhouse-00j.html

## Slide 27: Estimated Potential CO2 Disposal and Incremental Oil Recovery
(Assume 12Mcf CO2 per barrel of oil)

## Slide 28: CO2 Flooding: Oil Price Sensitivity
Base Case:
$20/bbl Oil
$1.00/mcf CO2
12% OOIP

## Slide 29: CO2 Flooding: CO2 Price Sensitivity
Base Case:
$20/bbl Oil
$1.00/mcf CO2
12% OOIP

## Slide 30: MIDCARB: Summary
Quality, Size and Geologic Integrity of Sequestration Sites (Safety and Longevity)
Location of Sequestration Sites Relative to CO2 Sources (Cost)
Relation of Quantity and Quality of CO2 Source to Sequestration Options
Economic Impact and Value of CO2 Recovery and Sequestration
Make Results Easily Available via Internet