## Slide 1: MIDCONTINENT INTERACTIVE DIGITAL CARBON ATLAS AND RELATIONAL DATABASE (MIDCARB)
Timothy R. Carr, James A. Drahovzal, Beverly Seyler, John A. Rupp, Scott W. White, and Lawrence H. Wickstrom
Notes: Current federal energy policy assumes that hydrocarbons will continue to be the primary source of energy for the United States and the world well into the 21st century. There is increasing concern about increasing atmospheric concentrations of carbon dioxide and its possible role in global climate change. For this reason, it may become necessary to manage anthropogenic CO2. Sequestering CO2 in geological reservoirs may be one way to safely sequester carbon over long periods of time, if the proper tools to analyze the geological feasibility as well as the associated costs can be developed.
The Midcontinent Interactive Digital Carbon Atlas and Relational DataBase (MIDCARB) will allow users to evaluate the quantity of sequestered CO2 in relation to a source supply, the security and safety of a site, and the long-term effects on a reservoir, as well as the cost of compression and transport of CO2 between source and sequestration site. MIDCARB will organize and enhance the critical information about CO2 sources and sequestration sites. Develops the technology needed to access, query, model, analyze, display, and distribute natural-resource data related to carbon management.

## Slide 2
Midcontinent
Interactive
Digital
Carbon
Atlas and
Relational
DataBase

## Slide 3: MIDCARB Project Goals
Intelligent & Efficient Database Access
Relational/Spatial Databases
  Local & Regional Level
Sources
  Quantity, Quality, Location
Sequestration Sites
  Security, Safety, Long-Term Effects
Costs & Benefits
Notes: MIDCARB will work across five mid-continent states with very different industrial, agricultural, demographic and natural resource characteristics. Work will concentrate on organizing and enhancing the critical information relative to CO2 sources and potential sequestration sites. Information such as the quantity, quality and location of sources relative to security, safety and long term effects on geologic sequestration sites. Finally we are developing information technology tools needed to access, query, model, analyze, display and distribute natural resource data related to carbon management across five states, various organizations and numerous databases. We are attempting to provide the basis to evaluate the potential technical feasibility, costs and benefits of any proposed carbon management plan at both the regional, state and even local level.

## Slide 4: MIDCARB Consortium
Notes: The project is a cooperative effort of five state Survey’s and DOE’s National Energy Technology Lab.

## Slide 5: State Perspective
Variation in Large Stationary CO2 Sources
Variation in Geologic Sequestration Opportunities
Distribution of Sources and Sinks
Significant and Differential Impact
  Among and Within States
  Economic Activity
  Energy Sources
Notes: Overall, the CO2 sequestration potential of the Midcontinent states of Illinois, Indiana, Kansas, Kentucky, and Ohio is large, but local variations suggest that any carbon management plan will have differential impact. Variations among states must be addressed (e.g., smaller oil and gas industry, but much larger coal industry). The spread of states in the proposed MIDCARB project has a wide range of populations, industry, agriculture, and fossil energy resources. Each of the five states in the MIDCARB consortium has a different mix and distribution of large, stationary CO2 sources and potential geologic sequestration opportunities. All states have a responsibility to attempt to reduce potential costs, maximize potential revenue, guard public safety, and assure long-term effectiveness of carbon management policies. Carbon management will have significant and differential effects on economic activity and fuels used for energy generation among states and even among regions within a single state. Viable carbon management will need the best local knowledge of local geologic and energy economic conditions.

## Slide 6: CO2 Power Plant Emissions MIDCARB Consortium
US Census Bureau and DOE/EIA

## Slide 7: Kansas Electrical Energy Consumption
423.7 Trillion Btu
Notes: Individual states, such as those in the MIDCARB consortium, will be on the front lines to develop cost-effective measurement, safety, and verification programs that best fit local conditions, but are acceptable to all involved (e.g., federal and state government regulators, carbon generator, auditors, public, non-government organizations, and repository operators).
It is reasonable for the states to have a strong understanding of the direct and indirect costs, risks, and benefits of operating under policies that constrain carbon emissions.
Illustrates the difference between two MIDCARB states in terms of electrical energy consumption. Indiana a much more populous state than Kansas is much more dependent on coal, a high carbon emission fuel, for electric generation.

## Slide 8: Indiana Electrical Energy Consumption
1165.4 Trillion Btu

## Slide 9: MIDCARB: Brings Together
Five Natural Resource Research Organizations
  Illinois, Indiana, Kansas, Kentucky, Ohio
Large Natural Resources Databases
Relational Database Management Systems
Geographic Information Systems
Network (Web) Expertise
http://www.kgs.ukans.edu/Midcarb
FOR MORE INFO...
Notes: MIDCARB will bring together the strength of five state geological surveys (i.e., Illinois, Indiana, Kansas, Kentucky, and Ohio). Each Survey is a proficient natural resource research organization that has demonstrated geographic information systems capabilities, and local experience with the fostering and monitoring of oil, coal and natural gas resources. Each state has large natural resource databases.
Generally, the required information is available from public sources, but is in a variety of formats intended to serve divergent purposes such as:
 evaluation of natural resources (e.g., oil, gas, coal, water, alternative energy, nuclear),
 management of industries (e.g., electric, oil and gas production, pipeline transportation, etc.),
 regulatory purposes (e.g., state oil and gas commissions, environmental protection, public safety and public utility boards)
 regional conditions (rural, urban, industrial, agricultural, etc.),
 research and technical foci (e.g., water quality, climate change, enhanced oil production, etc.), and
 taxation (natural resources tax data).

## Slide 10: MIDCARB: Available Resource Data
Oil
Gas
Coal
Water
Rock
Data

## Slide 11: MIDCARB: Brings Together
Five Natural Resource Research Organizations
  Illinois, Indiana, Kansas, Kentucky, Ohio
Large Natural Resources Databases
Relational Database Management Systems
Geographic Information Systems
Network (Web) Expertise
http://www.kgs.ukans.edu/Midcarb
FOR MORE INFO...
Notes: The consortium will use web-based standard queries and spatial database management systems to provide spatial and relational query capabilities for data loaded into relational database management systems (RDBMS). An example of present RDBMS systems includes the oil and gas query system of the Kansas Geological Survey. This RDBMS system allows the online user to query and join data contained in multiple tables for over 400,000 oil, gas and water wells. Queries are processed online and results returned as web pages. Due to programming within the RDBMS system, response times are extremely rapid.

## Slide 12: MIDCARB: Available Resource Data
RDMS
Oil
Gas
Coal
Water
Rock
Data

## Slide 13: MIDCARB: Brings Together
Five Natural Resource Research Organizations
  Illinois, Indiana, Kansas, Kentucky, Ohio
Large Natural Resources Databases
Relational Database Management Systems
Geographic Information Systems
Network (Web) Expertise
http://www.kgs.ukans.edu/Midcarb
FOR MORE INFO...
Notes: All five organizations involved in MIDCARB have demonstrated capabilities in geographic information systems (GIS), RDBMS, and web access. Geographic information systems allow users to compose customized maps consisting of selected spatially related data elements (i.e., themes). A theme is a map that shows data for a single subject matter. Examples of themes could include: (1) points showing locations of major CO2 sources, (2) lines showing existing pipelines, (3) polygons showing geologic sequestration reservoirs, and (4) images showing structural relief on a geologic horizon and reservoir net-pay thickness. In addition to displaying spatial data as maps, a GIS allows retrieval of descriptive information (attributes) about the geographic features in a theme. For example, one could develop a system that could not only view a map of major CO2 sources, but also by pointing to any given CO2 source with the cursor, retrieve the flue-gas data for that source. As part of the proposed project, the MIDCARB Consortium will develop an Internet Map Server (IMS) site and RDMBS focused on both CO2 sources and potential CO2 sequestration sites.

## Slide 14: MIDCARB: Available Resource Data
Applications
RDMS
Oil
Gas
Coal
Water
Rock
Data

## Slide 15: MIDCARB: Technology Approach
Information Technology Tools
  Relational Database Management Systems
  Geographic Information Systems
Advantages
  Data Maintained & Enhanced at Local Level
  Access & Assemble Data from Local Sources
  Provide Public Access to Data and Products
Challenges
  Coherent Data Across Organizations
  Coherent Data Across Scales
Notes: Work will also focus on designing adequate metadata standards to assure data quality and consistency.

## Slide 16: MIDCARB: Data Relationship Model
IL
IN
KY
KS
OH
Data

## Slide 17: MIDCARB: Technology Approach
Information Technology Tools
  Relational Database Management Systems
  Geographic Information Systems
Advantages
  Data Maintained & Enhanced at Local Level
  Access & Assemble Data from Local Sources
  Provide Public Access to Data and Products
Challenges
  Coherent Data Across Organizations
  Coherent Data Across Scales

## Slide 18: MIDCARB: Data Relationship Model
IL
IN
KY
KS
OH
Data
RDMS

## Slide 19: MIDCARB: A Different Approach
Data is Distributed
  Differences in Table Structure and Data Engines
Access is Uniform
  Web
  Online Query
  Online Mapping

## Slide 20: MIDCARB: Data Relationship Model
IL
IN
KY
KS
OH
Data
RDMS
Applications

## Slide 21: MIDCARB: Bringing It Together Online
Increased Scope & Breadth of Available Data
Improved Quality and Quantity of Data
Improved Accessibility
Scalable Access
Flexible Query Capabilities
Online Mapping
  Pre-selected and Custom Map Themes
Access Across Institution Boundaries

## Slide 22: MIDCARB: Data Relationship Model
IL
IN
KY
KS
OH
Data
RDMS
Applications
Networking

## Slide 23: CO2 Source Characterization
Flue Gas
  Pressure, Temperature, Concentrations, Output Patterns
Location (In relation to:)
  Sequestration Sites
  Transportation Infrastructure
Notes: On a national level, electricity generation is the major source of carbon emissions from stationary sources. Although electricity produces no emissions at the point of use, generation accounted for 37 percent of total carbon emissions in 1998, and its share is expected to increase to 38 percent in 2020.
The data needed to assess the CO2 resource of each state includes information on each stationary source (e.g. unit type, location, capacity size, energy source, and energy or fuel quantities). The research organizations involved in MIDCARB have strong relationships to state regulatory agencies, local organizations, and generating facilities in order to supplement publicly available information. Data on flue-gas pressure, temperature, gas concentrations, and output patterns (baseload, seasonal, or peaking). The acquisition of this data will require the cooperation of individual facilities and local organizations (e.g., public utility commissions). For those facilities that are unable to provide accurate information, reasonable estimates will be made based on fuel type, fuel characteristics (sulfur contents, heat content), and output-patterns history.

## Slide 24: Kansas: CO2 Emissions From Electric Generation Facilities

## Slide 25: Kentucky Power Plants
ê
Coal
Hydro
Fuel Oil
Natural Gas
ê
ê
ê
USEPA: E-GRID97, www.epa.gov/acidrain/egrid/egrid.html

## Slide 26: Kansas: CO2 Sources

## Slide 27: CO2 Sequestration Site Characterization
Oil Reservoirs
  CO2 Miscible and Immiscible Flooding
  Reservoir Fluid and Rock Properties
  Geologic and Engineering Data
Enhanced Gas Recovery and Coalbeds
Saline Aquifers
Conventional Gas Reservoirs
Unconventional Gas Reservoirs
Notes: This proposal concentrates on the geographic distribution and technical aspects of geologic storage options for CO2 sequestration, including those that recycle carbon back to its source in natural geologic formations. These include CO2 storage in geologic structures such as oil and gas reservoirs, coal seams, and saline aquifers.

## Slide 28: CO2 Geologic Sequestration Options
CO2 Improved Oil & Gas Recovery
CO2 Improved Coal Bed Methane Recovery
Deep Saline Aquifer
Underground Storage
Unmineable Coal
Modified from: http://www.spacedaily.com/news/greenhouse-00j.html

## Slide 29: Oil and Gas in Kentucky
TORIS

## Slide 30: Kentucky CBM Resource (Bcf)
130.2
153.4
Estimated from USGS 1995 National Assessment

## Slide 31: Kansas Production: Cumulative and CO2 Potential
Notes: Producing oil reservoirs offer some of the most attractive targets for CO2 sequestration. To evaluate the feasibility of CO2 miscible and immiscible flooding of oil reservoirs, a database of reservoir fluid and rock properties will be compiled for representative reservoirs. Critical technical variables include oil gravity, viscosity, minimum miscibility pressures (MMP), reservoir structure, depth, net pay thickness, porosity, permeability, irreducible water saturation, residual oil saturation after waterflood, relative fracture and matrix properties, and potential well-injection rates.
Much of this data is available in various databases from each of the five states in the MIDCARB consortium. However, critical variables such as the MMP and potential to achieve MMP in the reservoir are typically not available, but can be generated for representative reservoirs and reservoir fluids.

## Slide 32: Kansas: CO2 Potential Regional

## Slide 33: Kansas: CO2 Potential Local

## Slide 34: Oomoldic Porosity: Lansing-Kansas City ‘C’ Zone
1 cm

## Slide 35: Minimum Miscibility Pressure: Lansing-Kansas City Oils
Notes: The MMP is defined as the pressure where oil recovery ceases to increase significantly with increasing flooding pressure. At CO2 flooding pressures equal to or above the MMP, oil recovery is on the order of 90% of the oil in the portion of the reservoir contacted by the carbon dioxide. However, significant additional oil recovery can be achieved at pressures less than MMP.
As an example, technical data and assessment of the potential for application of CO2 miscible flooding in Kansas reservoirs was evaluated for pilot-site(s) appropriate to test and prove the CO2 flooding process. The MMP for several reservoir intervals in Kansas has been determined. The MMP for Lansing Kansas City (LKC) oils were measured from the Hall-Gurney Field, Russell County, Kansas. Tests indicate that MMP values are less than 1250 pounds per square inch (psi). A MMP of 1250 pounds is near the initial reservoir pressures of numerous LKC reservoirs in Kansas and appears achievable. Based on initial screening, application of CO2-miscible flood technology is technically feasible in Lansing-Kansas City reservoirs in central Kansas.

## Slide 36: Injector Sweep Efficiency : Lansing-Kansas City ‘C’ Zone
Notes: Relative simple and efficient streamtube simulations such as CO2 Prophet (USDOE, 1993) will be used to estimate oil recovery from carbon dioxide miscible and immiscible flooding in representative patterns (Figure 5). The initial calculations will be done in the square mile sections of high potential for a wide range of reservoir properties. Where possible, initial calculations will involve history that matches oil production from the preceding waterflood.

## Slide 37: Kansas: CO2 Sources
Notes: Economic models of carbon dioxide miscible and immiscible flooding will be developed using the screening calculations. Cost data will be developed for pilot-scale projects as well as representative field-wide and large-scale implementation. Economic feasibility will be determined by integrating cost projections with oil production predictions. Sensitivity calculations will be performed to identify the parameters that have a major influence on the technical and economic uncertainties in overall project economics.

## Slide 38: CO2 Flooding: Oil Price Sensitivity
Base Case:
$20/bbl Oil
$1.00/mcf CO2
12% OOIP

## Slide 39: CO2 Flooding: CO2 Price Sensitivity
Base Case:
$20/bbl Oil
$1.00/mcf CO2
12% OOIP

## Slide 40: CO2 Costs vs. Oil Price

## Slide 41: MIDCARB: Schedule
Project Underway (October 1, 2000)
Initial Database Access (1/01)
CO2 Source Characterization (9/01)
CO2 Sink Characterization (11/01 ongoing)
Web-Enabled Analysis & Display (Ongoing)
Technology Transfer (Ongoing)
FOR MORE INFO...
http://www.kgs.ukans.edu/Midcarb

## Slide 42: MIDCARB: Summary
Economic Impact and Value of CO2 Recovery & Sequestration
Quality, Size and Geologic Integrity of Sequestration Sites
Location of Sequestration Sites to Sources
Relation of Quantity & Quality of CO2 Source to Sequestration Options