## Slide 1: Application Of An Oil And Gas Fields Geographic Information System For CO2 Sequestration In Ohio
James McDonald, Ronald A. Riley, Lawrence H. Wickstrom, and Joseph G. Wells
Division of Geological Survey
Ohio Department of Natural Resources
April 4, 2002
Notes: ABSTRACT
A new geographic information system (GIS) for the oil and gas fields in Ohio is being used to determine the best candidates for geologic CO2 sequestration. Individual oil and gas fields have been defined by mapping individual areas of oil-and-gas production by producing geologic formations. By defining fields by the geologic formation, a more detailed approach can be made for assessing individual fields as potential candidates for CO2 sequestration and/or CO2-assisted enhanced recovery.
The oil and gas fields GIS will be linked with Ohio’s oil-and-gas-well data system, RBDMS (Risk-based Data Management System), and oil-and-gas production database, POGO (Production of Oil and Gas in Ohio), to allow greater flexibility of mapping and analyses. Linking of these databases will make it possible to dynamically update individual oil-and-gas field statistics and to modify or create field outlines as new drilling continues.
Each oil-and-gas field will contain associated attributes (where available) that include reservoir characteristics (e.g., average depth, lithology, porosity, permeability, reservoir temperature, and net thickness), production data (e.g., cumulative production, original-oil-in-place, and remaining-oil-in-place), and fluid characteristics (e.g., oil gravity, oil viscosity, and average water saturation). By relating these oil and gas field attributes, analyses will discern the best candidate fields for CO2 sequestration storability in depleted oil-and-gas fields and determine the oil-and-gas fields with the best potential for enhanced-recovery operations by injection of CO2.

## Slide 2: MIDCARB
Midcontinent
Interactive
Digital
Carbon
Atlas and
Relational
DataBase
Notes: This study is funded as part of the U.S. Department of Energy project, MIDCARB. MIDCARB stands for Midcontinent Interactive Digital Carbon Atlas and Relational dataBase. As explained in the two previous talks, there are many different methods for the geologic sequestration of CO2. For example, geologic sequestration can occur different sinks, such as oil & gas fields, coalbeds, and saline aquifers. This particular study focuses on the sequestration of CO2 in the oil & gas fields of Ohio.

## Slide 3: CO2 Sequestration - Depleted Oil and Gas Reservoirs
Trapping
  Same mechanisms that trapped original oil and gas
Benefits
  Proven trap
  Existing infrastructure
    Simpler
    Cheaper
  Storage over geologic time periods
MIDCARB data
  Reservoir fluid and rock properties
  Geologic and engineering data

## Slide 4: CO2 Sequestration - Active Oil and Gas Reservoirs
CO2 flooding (EOR activities)
  Miscible and immiscible in oil reservoirs
  Possible pressure maintenance in gas reservoirs
Benefits
  Increase oil and gas production
  Sequester CO2: lower net cost for sequestration
Extensive industry CO2 EOR experience and data
MIDCARB data
  Reservoir fluid and rock properties
  Geologic and engineering data

## Slide 5: Ohio’s Oil & Gas Fields
Notes: I would like to give you some background about Ohio’s oil & gas fields.
Production began in 1860, continues to present
Over 257,000 wells drilled in Ohio
  Provides information on reservoir parameters
  Over 80,000 geophysical logs – provide reservoir parameters
  Fluid samples from the oil & gas wells, provide information needed for solubility, adsorption, and hydrodynamic trapping
Over 1000 oil & gas fields in the state
Mapping of the Oil & Gas Fields was conducted 1909, 1948, 1953, 1960, 1964, 1974, and most recently, 1996

## Slide 6: Ohio Oil & Gas Field GIS
Created as part of the U.S. DOE funded Atlas of Major Appalachian Gas Plays and TORIS projects
Mapped pool & field outlines by geologic formation
Grouped by play
Field outlines stored digitally in CAD format
Field attributes stored in separate database
Notes: Oil & gas field maps created from the 1996 Appalachian basin gas atlas
Work digitally created in CAD format
Attributes for the GIS were created from the oil & gas field spreadsheet.
Funded by the U.S. Department of Energy and compiled primarily by partners of the Appalachian Oil and Natural Gas Research Consortium (state geological surveys of Kentucky, Ohio, Pennsylvania, and West Virginia, and the University of West Virginia), the Atlas of Major Appalachian Gas Plays provides a comprehensive description of 30 major gas plays in the basin. A companion digital database containing geologic and engineering data on gas fields and reservoirs within each play also is available. The Atlas contains hundreds of illustrations depicting stratigraphy, structure, geophysical profiles, and reservoir and production information for all major fields and pools.
The Atlas describes and illustrates the geology of 30 major gas plays in the Appalachian Basin, seven of which occur dominantly in Ohio. The Atlas project has greatly increased geologic knowledge of natural gas resources for the Appalachian Basin portion of Ohio and surrounding areas and provides essential information for exploration and development of the region's natural gas resources.

## Slide 7: Ohio Oil & Gas Field GIS
Oil & gas field attributes in separate data file for many of the fields
  Merged Gas Atlas and TORIS databases
Converted to GIS format
  Converted CAD files to coverages
  Joined field data file to the GIS coverage attribute table
Oil & Gas fields are separated by geologic unit
Notes: 1. Oil & gas field parameters in separate data file for many of the fields
Converted to GIS format
  Converted CAD files to coverages
  Joined field data file to the GIS coverage attribute table
Oil & gas field parameters in separate data file for many of the fields
Converted to GIS format
  Converted CAD files to coverages
  Joined field data file to the GIS coverage attribute table
Fields are separated by geologic unit
Converted CAD files to GIS format
Merged gas atlas and TORIS databases
Joined DB table with the GIS files
Renaming the fields (ongoing)

## Slide 8: GIS Advantages
Attributes queries
Spatial queries
Overlay operations
Calculations and Testing Scenarios
Notes: Query attributes
Spatial queries
Overlay operations
Modeling and calculations

## Slide 9: Querying Attributes
Notes: In this slide, I have an example of querying the GIS database for a particular attribute. I have queried the database table for depth greater than 3000 feet. This particular parameter is important for determining whether CO2 will be injected either as a gas or a supercritical liquid.

## Slide 10: Simple CO2 Sequestration Calculation
Notes: In this next slide, we have a simple example of the amount of CO2 sequestration in oil & gas fields that can be calculated using geographic information systems (GIS) technology. In this slide, the Clinton sandstone oil & gas pools GIS layer is displayed. Each pool in the GIS layer is represented by a color filled polygon and each of the polygons is tied to a record in the attribute table. Each pool has many different attributes associated with it, such as Average Thickness, Average Porosity, and Original Oil In Place. Using the attributes associated with each polygon, calculations can be made as to how much CO2 can be sequestered in each oil & gas pool. These calculations are now an attribute associated with each polygon in the GIS. Highlighted in yellow, this pool of the Canton Consolidated oil & gas field can sequester over 51 billion tons of CO2

## Slide 11: Some Important Reservoir Characteristics
General reservoir characteristics
  Depth, Temperature, Pressure, Drive Mechanism
Geological characteristics
  Structure and Seal, Diagenesis
Engineering
  Well spacing, well-bore integrity
Rock-fluid properties
  Porosity & permeability
Notes: General reservoir characteristics
  Reservoir depth
  Temperature
  Pressure
  Reservoir drive mechanism
Geological characteristics
  Structure and reservoir seal
  Diagenisis/mineralogy
Engineering and reservoir development characteristics
  Well spacing
  Well-bore Intergrity
  Waterflooding
  Pressure Depletion
Rock-Fluid Properties
  Oil & Gas Gravity
  Porosity and Permeability
  Irreducible Water and Residual Oil Saturation
  Relative Permeability
  Injectivity

## Slide 12: Example - General Reservoir Characteristics
Notes: Generally, for CO2 EOR operations, the reservoir pressure must be above 1000 psi. As can be seen in this slide, all of the Clinton sandstone oil & gas fields are below 1000 psi. For EOR operations to take place, they would have to be repressurized, possibly by waterflooding. For an operator, it might be more economical to work with the reservoirs that are currently higher pressurized.

## Slide 13: Example – Rock/Fluid Properties
Notes: Permeability, the ease at which fluid flows through a rock, determines the fluid dynamics of the reservoir. High permeability will allow high volumes of CO2 to be injected into a single well, thus reducing cost. High permeability will also allow CO2 to move more quickly into the reservoir, which is also favorable to sequestration. In this slide, we can see that the Clinton sandstone is a low permeability unit. Thus the costs of sequestering CO2 will be far higher for this unit than some other geologic unit.

## Slide 14: Screening Criteria For Co2 Miscible Flooding In Appalachian Area (Watts, 1985)
Oil Viscosity (cp) < 12 cp
API Gravity > 25o
Residual Oil Saturation > 20 Percent
Depth (Ft) > 1,800-2,000 ft
Net Pay (Ft) > 10
Operating Pressure > 1,000 psi
Well Spacing Critical
Reservoir Heterogeneity Critical

## Slide 15: Example – Screening Criteria
Notes: In this slide, I have used some of the screening criteria from Watts (1985). The criteria that I have used to search for candidate fields is depth > 1800 feet, Net Pay > 10 feet, and Current Pressure > 1000 psi. The search criteria has identified the Canton Consolidated field as a potential candidate for EOR operations.

## Slide 16: Summary & Conclusions
Creation Oil & Gas Fields GIS for Ohio
Over 500 oil & gas fields (out of the over 1000 fields) have average data calculated
GIS can be queried for specific attributes values
Spatial analysis
Test Different Scenarios