## Slide 1: Characterization of a Deep Saline Aquifer for CO2 Sequestration in Indiana:
An Integrated Geology/GIS Approach
Wilfrido Solano-Acosta
Nathan K. Eaton
Indiana Geological Survey
Indiana University, Bloomington
Notes: More than 99% of the power generated in Indiana is derived from coal-fired plants. As byproduct, large amounts of CO2 and other flue-gases are produced from these facilities, as well as from other types of industry (i.e. steel mills, refineries, etc). Due to the potential environmental effects produced by the release of these gases, there is a need to find adequate sites for safely storing them.
Geological formations represent the most appropriate sites for storing large volumes of CO2 and other flue-gases. The deep brine-filled aquifers are considered to have the highest potential for CO2 sequestration, for that reason, an attempt to characterize one such aquifer is presented here.

## Slide 2: Introduction
Aquifer characterization
  TDS
  Thickness (of porous zones)
  Porosity
Estimate net pore volume (for CO2 storage)
Notes: This presentation is divided into three main parts:
A brief overview of the regional distribution of the Hunton aquifer in the study area.
Some characteristics of the aquifer are presented, such as TDS, thickness of the porous intervals, and porosity of such intervals.
An example of the procedures followed to estimate the net pore volume available in the porous intervals described.
The results presented here are the preliminary evaluation of a brine-filled aquifer.

## Slide 3
Notes: This map shows the extent of the edge of the Devonian in Indiana, and the southernmost portion corresponds to the area where data was measured.
The Hunton aquifer was chosen for this study and corresponds to the Silurian-Devonian carbonate section of Indiana.
Previous studies in the area from Rupp and Pennington (1987), Mitchell and Rupp (1994), and Schnoebelen et al (1995) provided data on the distribution of the total dissolved solids in Indiana, and particularly on the location of the 10,000 ppm TDS. In such works, these authors suggested that the Silurian-Devonian stratigraphic section behaves as a single hydrodynamic unit.

## Slide 4
Upper Middle Devonian
Lower Middle Devonian
Silurian
Notes: The Ordovician Maquoketa and Upper Devonian New Albany shales represent the vertical barriers to flow and are considered the confining units of the Hunton aquifer.
The Hunton aquifer in Indiana is characterized by the lithostratigraphic units shown on the left column, with porous intervals particularly within the Upper-Middle Devonian (North Vernon limestone), and the dolomitic intervals of the Jeffersonville/Geneva, and the Silurian reefs. The Silurian reefs are normally well developed in the upper Silurian Wabash Formation and the Salamonie dolomite.
The yellow stars represent intervals with dolomitic porosity. Such type of porosity is clearly identified in density logs as will be shown in a couple of cross sections through the study area.

## Slide 5
Notes: This slide shows the distribution of the data points used for this study. A total of 38 wells with information down to the Cincinnatian were used to construct two cross-sections in order to observe the regional distribution of the Hunton facies and its porosity.
As a reference, the outline of the Silurian Terre Haute reef bank (Ault et al., 1987) is shown; within these polygons, pinnacle reefs are irregularly distributed.
Section A-A’ is based on well-log data from Greene, Daviess, Knox, Gibson, and Posey counties.

## Slide 6
Notes: Significant porosity intervals are observed in some places, in particular those associated with dolomites and reefs.
Note that high porosity intervals are rather discontinuous and patchy as expected in pinnacle reefs.
High porosity intervals are particularly well developed in Greene , Daviess, and Knox counties. Porosity is drastically reduced with depth in the basin.
Zones with porosity higher than 5% were colored to observe the distribution of porosity in the basin.
Lower Devonian facies pinch out to the east. In these facies, porosity is irregularly distributed.

## Slide 7
Notes: Section B – B’ includes information from Jackson, Washington, Orange, Perry, and Spencer counties.

## Slide 8
Notes: This section clearly indicates its proximity to the basin edge, showing considerable thinning of the carbonate facies. Also note that porosity is also better developed in both dolomitic and non-dolomitic zones.
In the Upper Middle Devonian, near the basin edge, good porosity is present, but decreases rapidly with depth in the basin.
Same occurs for the Lower Middle Devonian, and Silurian.
Again, Lower Devonian pinches out to the east as shown in the previous cross section (A – A’).

## Slide 9: Methods
Geophysical well logs
  Dual induction (resistivity)
  Compensated density
Porosity/Resistivity and Formation Factor
Grid analysis
  ArcView Spatial Analyst
  ArcInfo Grid module
Notes: The methods used in this study included readings from Geophysical well logs, particularly dual-induction and compensated density logs, which were used to characterize the Hunton aquifer. The rationale for using density and resistivity logs was two-fold:
1) to identify the porous intervals of the Middle Devonian and Silurian and,
2) to calculate the NaCl equivalent TDS concentration based on log-derived information.
TDS values were calculated with the porosity/resistivity and the Formation Factor methods (Rupp and Pennington, 1987)
The existing information on brine chemistry from water sample analyses was not included in this study because it was not possible to establish accurately the specific porous zones within the Silurian-Devonian from which the samples were derived.
Point data were interpolated into grids with cells of 2 by 2 kilometers using the inverse distance weighted algorithm of the Spatial Analyst extension of ArcView 3.2.
Grid calculations (pore space, net thickness) were performed with the Grid module in ArcInfo.

## Slide 10
Notes: Based on the well-log data, TDS calculations for each zone of interest were performed and showed good correlation between both resistivity/porosity and Formation Factor methods.
For porosity intervals of less than 4 – 5%, the algorithms did not work correctly, and highly anomalous TDS values were obtained.
The red line corresponds to the 10,000 ppm TDS boundary according to Schnoebelen et al (1995). Schconebelen’s line was constructed on the basis of the first appearance of TDS concentration greater than 10,000 ppm, regardless of the stratigraphic interval. For that reason, the same line is shown in all diagrams to observe the correlation between Schnoebelen’s dataset and ours.

## Slide 11
Notes: This slide compares the average TDS values for the Hunton aquifer, with the 10,000 ppm TDS boundary proposed by Schnoebelen et al (1995). Good correlation between both datasets can be observed.

## Slide 12
Notes: Net thickness maps for the porous intervals of each zone of interest were generated.
The red line corresponds, again, to the regional distribution of the Silurian Terre Haute reef bank according to Curt Ault et al (1987).
The Silurian section presents the largest porous thickness interval followed by the Lower Middle Devonian and Upper Middle Devonian respectively.

## Slide 13
Notes: This slide synthesizes the net porous thickness of the Hunton aquifer in the study area by simply summing the individual porous unit thicknesses.

## Slide 14
Notes: In this slide, the distribution of porosity for each zone of interest for the Hunton aquifer is presented.
Overall, the zones with greater porosity are those in the Silurian and Lower Middle Devonian, in other words, the zones with dolomitic porosity.

## Slide 15: Net pore Volume Calculation
An example
Notes: From now to the end of this presentation, the overall procedure for calculation of net pore volume for one of the interest zones is presented, in this case the Upper Middle Devonian (North Vernon Limestone). Finally, a summary of the total pore volume estimated for the Hunton aquifer of SW Indiana will be shown.
The porosity estimated represents the total intergranular/intragranular volume predicted with the GIS gridding algorithm for the porous zones identified in three main intervals, one in Upper Middle Devonian, one in Lower Middle Devonian, and a Silurian one.

## Slide 16
Notes: Based on the net porous thickness map produced for the Upper Middle Devonian and

## Slide 17
Notes: the porosity distribution, which presents a regional trend of decrease in porosity towards the basin,

## Slide 18
Notes: the calculation consisted in multiplying the grids thickness, porosity, and area, using the grid module of ArcInfo, to obtain

## Slide 19
Total pore volume ~ 0.17 TCF
Notes: a grid with discrete values of net pore space for each 2 by 2 Km cell.
Note how the pore space decreases with depth in the basin.
The total pore volume calculated for the Upper Middle Devonian porous section is approximately 0.17 TCF.
Remember: The total estimated pore volume corresponds to the net void intergranular/intragranular space, and does not include fracture, vug, and karst porosity, which may significantly increase the available space for CO2 storage.

## Slide 20
Notes: In this slide we observe the calculation of Upper Middle Devonian presented before. It is also a summary for the three zones of interest.
Same type of analysis was done for the other two intervals (Lower Middle Devonian, and Silurian)
Finally, in order to estimate the net pore volume for the Hunton aquifer, the individual volumes were added using the same ArcInfo Grid module

## Slide 21
Total pore volume ~ 1 TCF
Notes: Obtaining a final value of net pore volume of nearly 1 TCF for the Hunton Aquifer in SW Indiana.

## Slide 22: Conclusions
Hunton aquifer
  Upper Middle Devonian
  Lower Middle Devonian
  Silurian Reefs
TDS distribution observed correlates well with the 10,000 ppm line proposed by Schnoebelen et al (1995)
~1 TCF of net pore volume is available in the Hunton aquifer for CO2 sequestration in the study area
Notes: The Hunton aquifer of SW Indiana has three porous zones, one in the Upper Middle Devonian, one in the Lower Middle Devonian, and one or two in the Silurian.

## Slide 23: Characterization of a Deep Saline Aquifer for CO2 Sequestration in Indiana:
An Integrated Geology/GIS Approach
Wilfrido Solano-Acosta
Nathan K. Eaton
Indiana Geological Survey