## Slide 1: Modeling of CO2 – Brine – Rock Reaction in a Mixed Carbonate – Siliciclastic Aquifer B. Zerai, B. Saylor and G. Matisoff Case Western Reserve University

## Slide 2: Introduction
Geologic sequestration is a promising idea to reduce emissions of CO2. The success requires the ability to:
  Capture
  Transport
  Inject and store
    Main issue - Geochemical reactions between deep aquifer brine, formation minerals, and injected CO2.
Notes: Explain briefly the need for reduction of Greenhouse gases
Explain briefly the three points
Emphasis that the present paper is focused on Geochemical reactions

## Slide 3: Geochemical Modeling of Fluid-Rock Reactions in No-Flow Conditions
Geochemical effect of CO2 injection into deep saline aquifer
Extent of CO2 immobilization via carbonate precipitation
Major concern -- What will happen to the CO2 injected into a deep aquifer?
      Will it sequester as solid rock?
      Will it be trapped ‘hydrodynamically’ in the aquifer?
Notes: Give some insight about what you are doing and what should be done to fully explain the underlined problem
Again make your point that the focus of the paper is Geochemical modeling
Briefly state the situation in modeling in light of CO2 gas

## Slide 4: Geochemical Trapping
  Solubility trapping
    CO2(g) H2CO3 (aq)
    CO2(g) CO2 (aq)
  Ionic trapping
    H2CO3 (aq) + OH- HCO3- (aq)
    HCO3 (aq) + OH- CO32- (aq)
  Mineral trapping
    CO32-(aq) + Ca2+ CaCO3 (Solid)
    HCO3- + Fe2+ FeCO3 (Solid)
    HCO3- + 2H2O + Na+ + Al3+ NaAlCO3(OH)2 (Solid) + H+
Notes: What are the possible mechanism for injected CO2 gas to be trapped or sequestered? Explain briefly

## Slide 5
Rose Run
Hansen (1997), Riley et. al. (1993), Janssens et al. (1973)
Lies at more than 800 m depth
Overlain by low permeable rocks
Regional flow is down dip (SE)
Composed of Carbonate and Siliciclastic rocks
Rose Run Sandstone
Notes: Introduce to the audience the geology of interest and its stratigraphic position
Introduce the site of interest and its geological stratigraphy. Explain why it is choosen
Black River, Trenton, Cincinnatian strata – serve as the low permeable overlying rocks

## Slide 6: Mineral Composition of Rose Run Carbonate Siliciclastic
Dolomite K-feldspar
Calcite Kaolinite
Siderite Albite
Quartz
Annite
Siderite
Major Ions (mg/kg) - Ca2+, Mg2+, Na+, K+, HCO3-, Cl-, SO42-, Al3+, SiO4(aq), Fe2+
pH - 6.5 Temperature - 50o C
Parameters
Lowry and Faure (1988), Janssens et al. (1973)
Notes: Introduce the the mineralogical composition of each assemblage. Mention that Annite is replaced in the place of Glauconite
Without going to much into details, explain the source of the brine (Clinton Sandstone) and the values of the other variables
T=50, Porosity=15-20%, pH=6.5

## Slide 7: Method
The CO2-brine-rock reaction of the Rose Run Sandstone was modeled using Geochemist’s Workbench (GWBTM) under thermodynamic equilibrium
Notes: Introduce what kind of software u r using and give brief explanation about the assumptions made

## Slide 8
The injected CO2 pressure decreases as a function of radial distance.
  Does the pattern of reaction mimic the same trend?
What is the effect of different formation water chemistry on the outcome of the reaction?
Questions to Address
Injected CO2(g)
  Carbonate Rocks
  Siliciclastic Rock
Decrease in fugacity
Notes: Explain briefly that the Rose Run Formation has different mineral assemblages and state that the picture does not imply stratigraphic sequence. Just subdivided to model and understand the different possible reactions.

## Slide 9: Results
Carbonate Aquifer
Precipitate
Dissolve
Notes: Start with Carbonate aquifer and explain pH and HCO3 species concentration in the brine as a function of fugacity.
Point out the how the total mass tend to dissolve with an increase in fugacity of CO2

## Slide 10
Calcite + H2O + CO2 Ca2+ + 2HCO3-
4HCO3- + Ca2+ + Mg2+ Dolomite + 2CO2(g) + 2H2O
HCO3- + Fe2+ Siderite + H+
Carbonate Aquifer
Precipitate
Dissolve
Notes: Explain the possible chemical rxns.

## Slide 11
Carbonate
Most of the CO2 is trapped as bicarbonate and as dissolved CO2 (aq).
The fugacity at the end of the reaction is around 100 atmosphere. If the confining pressure < 100 Blow out

## Slide 12: Siliciclastic Aquifer
Precipitate
Notes: Mention – the total mass is still on the precipitation side

## Slide 13
Siliciclastic Aquifer
Precipitate
Precipitate
Notes: Explain the minerals formed and point out that unlike the carbonate assemblage, calcite is produced as a result of Ca++ species in brine and the introduction of gas

## Slide 14
3 Annite + 7CO2(g) + H2O 3 Siderite + 3 Quartz + Al3+ + K+ + 4HCO3-
K-feldspar + Na+ + CO2 (aq) + H2O Dawsonite + 3 Quartz + K+
3 K-feldspar + 2H2O + 2CO2(g) 2K+ + Muscovite + 6 Quartz
+ 2HCO3-
Albite + 2H2O + 2CO2(g) + K+ Na+ + Muscovite + 6 Quartz + 2HCO3-
Kaolinite + 4SiO2 + 2K+ + 2HCO3- 2 Microcline + 3H2O
+ 2CO2(g)
Notes: Explain the possible rxns one by one and mention the total dissolution of K-feldspar, Kaolinite, Albite and Annite

## Slide 15
Siliciclastic
Considerable amount of Siderite and Dawsonite and small amount of Calcite and Dolomite are formed.
CO2 is trapped in mineral form.

## Slide 16: Varying Brine Composition: Siliciclastic Aquifer

## Slide 17: Siliciclastic Aquifer : Aqueous Species

## Slide 18
Siliciclastic Aquifer : Carbonate precipitation

## Slide 19: Conclusions
Solubility and ionic trapping are favored in Carbonate Aquifer.
Mineral trapping is favored in Siliciclastic Aquifer.
The extent of mineral and solubility trapping strongly depends on formation mineralogy, brine chemistry, and fugacity.